| 2010 "LSA" 6.2L V-8 SC ( LSA ) | 6/5/2009 |
| --- | --- |
| Type: | 6.2L Gen IV V-8 Small Block |
| Displacement: | 6162 cc (376 ci) |
| Engine Orientation | Longitudinal |
| Compression ratio: | 9.1:1 |
| Valve configuration: | Overhead valves (2 valves per cylinder) |
| Assembly site: | Silao, MX |
| Valve lifters: | Hydraulic roller |
| Firing order: | 1 - 8 - 7 - 2 - 6 - 5 - 4 - 3 |
| Bore x stroke: | 103.25 x 92 mm |
| Fuel system: | Sequential fuel injection |
| Fuel Type: | Premium required |
| Maximum Engine Speed: | 6200 RPM |
| Emissions controls: | Catalytic converter |
|  | Three-way catalyst |
|  | Positive crankcase ventilation |
| Valves per cylinder | 2 |
| Bore Center (mm) | 111.76 |
| Applications: | Horsepower: hp ( kw ) |
| Cadillac CTSV | 556 hp ( 415 kW ) @ 6100 rpm SAE CERTIFIED |
| Applications: | Torque: lb-ft ( Nm ) |
| Cadillac CTSV | 551 lb-ft ( 747 Nm ) @ 3800 rpm SAE CERTIFIED |
| MATERIALS |  |
| Block: | Cast aluminum |
| Cylinder head: | A356-T6 rotocast cast aluminum |
| Intake manifold: | Cast aluminum |
| Exhaust manifold: | High silicon / high moly cast iron |
| Main bearing caps: | Nodular Iron |
| Crankshaft: | Forged steel |
| Camshaft: | Hollow steel |
| Connecting rods: | Forged powder metal |
| Additional features: | 1.9 L/rev Supercharger |
|  | Integrated single coolant to air intercooler |
|  | Piston oil spray cooling |
|  | Direct mount ignition coils |